## Slide 1: Data packages
Basic information in addition to full list

## Slide 2: Basic information
Data package is a set of outgoing data from eSett’s point of view towards the Market Participants, which the Market Participants has subscribed to receive.
Data packages contain imbalance settlement data for Market Participants that are entitled to see them (DSOs and BRPs).
eSett defines the data content of the data packages in addition to from which time period and when information is sent to Market Participants.
List of available data packages is published in Online Service, from this list Market Participants are able to subscribe to those which they prefer.
The data packages are sent to Market Participants automatically either based on certain timing or process being finalized. E.g. once a day at certain time after the data regarding the open and final imbalance settlement period has been processed.
Note that there might be same data packages but in different resolution i.e., 15 min or 1 hour
Some data packages do not have broader description but the name should be fairly descriptive of the contents
Data packages will be divided to specific and generic ones
  Specific data packages will utilize the same data flow formats as Information Service.
  Generic data packages will utilize generic format.

## Slide 3: Specific data packages; hourly values on a daily basis 1/8
Data Package | Description | MP Role
Tertiary Replacement Reserves (RR) | All BRP's activated reserves of type RR (Tertiary Control) | BRP
Secondary Frequency Restoration Reserves (FRR) | All BRP's activated reserves of type FRR-A (Frequency Restoration Reserve - Automatic) | BRP
Primary Frequency Containment Reserves (FCR) | All BRP's activated reserves of type FCR (Frequency Containment Reserve) | BRP
Bilateral Trade Final Confirmation Report | Bilateral trades under BRP's balance responsibility | BRP
Bilateral trades | Bilateral trades under BRP's balance responsibility | BRP
Primary Frequency Containment Reserves (FCR) – contracted reserves | All BRP's contracted reserves of type FCR (Frequency Containment Reserve). | BRP
Tertiary Replacement Reserves (RR) – contracted reserves | All BRP's activated reserves of type RR (Tertiary Control) | BRP
Secondary Frequency Restoration Reserves (FRR) – contracted reserves | All BRP's activated reserves of type FRR-A (Frequency Restoration Reserve - Automatic) | BRP

## Slide 4: Specific data packages; hourly values on a daily basis 2/8
Data Package | Description | MP Role
Metering Grid Area (MGA) losses per MGA | All DSO's metering grid areas' (MGA) losses per MGA | DSO
REs' consumption data per type and MGA (evening) | All BRP's responsibility MGAs' REs' consumption data per type and MGA | BRP
REs' consumption data per type and MGA | All DSO's MGAs' REs' consumption data per type and MGA | DSO
REs' consumption data per type and MGA | All BRP's responsibility MGAs' REs' consumption data per type and MGA | BRP
Consumption imbalance per BRP per MBA (volume and amount) | BRP's consumption imbalance volumes (MWh) and amounts (EUR) per MBA | BRP
Imbalance – Invoiced Results | DP contains BRP production imbalance results for all respective MBAs and period in CET. | BRP
Imbalance – Final Results | DP contains BRP production imbalance results for all respective MBAs and period in CET. Calculations are per couple BRP and MBA. | BRP

## Slide 5: Specific data packages; hourly values on a daily basis 3/8
Data Package | Description | MP Role
Imbalance per BRP per MBA (Volume and Amount) | BRP's imbalance volumes (MWh) and amounts (EUR) per MBA | BRP
Imbalance – Preliminary Results | DP contains BRP production imbalance results for all respective MBAs and period in CET. Calculations are per couple BRP and MBA. | BRP
REs' Merged Production Data per Type and MGA (evening) | All BRP's responsibility REs' merged production data per type and MGA | BRP
REs' Merged Production Data per Type and MGA | All BRP's responsibility REs' merged production data per type and MGA | BRP
REs' Merged Production Data per Type and MGA | All DSO's metering grid areas' (MGA) per MGA, Production Type and Production Unit Type | DSO
MGA Exchanges | All DSO’s MGA Exchanges | DSO
MGA Imbalance – Final Results |  | BRP
MGA Imbalance – Preliminary Results |  | BRP
MGA Imbalances | All DSO's MGAs' imbalances per MGA | DSO

## Slide 6: Specific data packages; hourly values on a daily basis 4/8
Data Package | Description | MP Role
MGA Imbalances (evening) | All MGAs' imbalances per MGA under BRP's balance responsibility | BRP
MGA Imbalances | All MGAs' imbalances per MGA under BRP's balance responsibility | BRP
MGA Imbalance – Invoiced Results |  | BRP
MGA Imbalance – Preliminary Results |  | DSO
MGA Imbalance – Final Results |  | DSO
MGA Exchange Final Confirmation Report |  | DSO
MGA Exchange Intermediate Confirmation Report |  | DSO

## Slide 7: Specific data packages; hourly values on a daily basis 5/8
Data Package | Description | MP Role
Consumption MEC (Delta) | DSO’s Consumption MECs starting or ending within the configured time period. | DSO
MGA Imbalance Retailer (Active) | All DSO’s MGA Imbalance Retailers which are valid sometime within the configured Period. | DSO
MGA Imbalance Retailer (Delta) | All DSO’s MGA Retailers starting or ending within the configured period. | DSO
BRP’s Consumption MEC (Delta) | BRP’s Consumption MECs starting or ending within the configured time period | BRP
Retailer Balance Responsibility - All | Retailer Balance Responsibilies valid sometime in upcoming 14 days (at least some period) | DSO
BRP’s Consumption MEC (Active) | BRP’s Consumption MECs which are valid sometime within the configured period. | BRP
Retailer Balance Responsibility - Delta | Retailer Balance Responsibilies starting or ending in upcoming 14 days | DSO

## Slide 8: Specific data packages; hourly values on a daily basis 6/8
Data Package | Description | MP Role
Consumption MEC (Active) | DSO’s Consumption MECs which are valid sometime within the configured period. | DSO
Imbalance prices per Market Balance Area (MBA) | BRP's production imbalance volumes (MWh) and amounts (EUR) per MBA | BRP
Production per production unit (PU) | All DSO's productions per production unit (PU) | BRP
Production per production unit (PU) (evening) | All productions per production unit under BRP's balance responsibility | BRP
Production per production unit (PU) | All productions per production unit under BRP's balance responsibility | DSO
Production imbalance per BRP per MBA (volume and amount) | BRP's production imbalance volumes (MWh) and amounts (EUR) per MBA | BRP
Production Imbalance - Preliminary Results |  | DSO
Bilateral Trade Intermediate Confirmation Report |  | BRP

## Slide 9: Specific data packages; hourly values on a daily basis 7/8
Data Package | Description | MP Role
Production Imbalance – Invoiced Results |  | DSO
Production Imbalance – Final Results |  | BRP
Production plan per BRP and RO | All BRP's production plans per RO | BRP
PX Trades - Day-ahead (NSL) |  | BRP
PX Trades - Day-ahead |  | BRP
PX Trades - Intraday |  | BRP
Imbalance prices per Market Balance Area (MBA) | Production and Consumption imbalance prices per MBA | BSP

## Slide 10: Specific data packages; hourly values on a daily basis 8/8
Data Package | Description | MP Role
Production Units (Active) | DSO’s Production Units which are valid sometime within the configured time period. | DSO
Production Units (Delta) | DSO’s Production Units starting or ending within the configured time period | DSO
Secondary Frequency Restoration Reserves (FRR) | All BSP's activated reserves of type FRR-A (Frequency Restoration Reserve - Automatic) | BSP
Tertiary Replacement Reserves (RR) | All BSP's activated reserves of type RR (Tertiary Control) | BSP
Primary Frequency Containment Reserves (FCR) | All BSP's activated reserves of type FCR (Frequency Containment Reserve) | BSP
Primary Frequency Containment Reserves (FCR) – contracted reserves | All BSP's contracted reserves of type FCR (Frequency Containment Reserve) | BSP
Tertiary Replacement Reserves (RR) – contracted reserves | All BSP's activated reserves of type RR (Tertiary Control) | BSP
Secondary Frequency Restoration Reserves (FRR) – contracted reserves | All BSP's activated reserves of type FRR-A (Frequency Restoration Reserve - Automatic) | BSP

## Slide 11: Specific data packages; 15 min values on a daily basis 1/5
Data Package | Description | MP Role
Bilateral Trade Intermediate Confirmation Report |  | BRP
Bilateral Trade Final Confirmation Report |  | BRP
Bilateral trades | Bilateral trades under BRP's balance responsibility | BRP
Metering Grid Area (MGA) losses per MGA | All DSO's metering grid areas' (MGA) losses per MGA | DSO
REs' consumption data per type and MGA (evening) | All BRP's responsibility MGAs' REs' consumption data per type and MGA | BRP
REs' consumption data per type and MGA | All DSO's MGAs' REs' consumption data per type and MGA | DSO
REs' consumption data per type and MGA | All BRP's responsibility MGAs' REs' consumption data per type and MGA | BRP
Imbalance – Preliminary Results | DP contains BRP production imbalance results for all respective MBAs and period in CET. Calculations are per couple BRP and MBA. | BRP
Imbalance – Invoiced Results | DP contains BRP production imbalance results for all respective MBAs and period in CET. Calculations are per couple BRP and MBA. If BRP Branch has different preferred currency from EUR, then the file contains results in local currency and also results in EUR currency. | BRP
Imbalance – Final Results | DP contains BRP production imbalance results for all respective MBAs and period in CET. Calculations are per couple BRP and MBA. | BRP
Imbalance per BRP per MBA (Volume and Amount) | BRP's imbalance volumes (MWh) and amounts (EUR) per MBA | BRP

## Slide 12: Specific data packages; 15 min values on a daily basis 2/5
Data Package | Description | MP Role
REs' Merged Production Data per Type and MGA | All DSO's metering grid areas' (MGA) per MGA, Production Type and Production Unit Type | DSO
REs' Merged Production Data per Type and MGA | All BRP's responsibility REs' merged production data per type and MGA | BRP
REs' Merged Production Data per Type and MGA (evening) | All BRP's responsibility REs' merged production data per type and MGA | BRP
MGA Exchanges | All DSO’s MGA Exchanges | DSO
MGA Imbalance – Final Results |  | BRP
MGA Imbalances | All DSO's MGAs' imbalances per MGA | DSO
MGA Imbalance – Invoiced Results |  | BRP
MGA Imbalances | All MGAs' imbalances per MGA under BRP's balance responsibility | BRP
MGA Imbalances (evening) | All MGAs' imbalances per MGA under BRP's balance responsibility | BRP
MGA Imbalance – Final Results |  | DSO
MGA Imbalance – Preliminary Results |  | DSO
MGA Imbalance – Preliminary Results |  | BRP

## Slide 13: Specific data packages; 15 min values on a daily basis 3/5
Data Package | Description | MP Role
MGA Exchange Final Confirmation Report |  | DSO
MGA Exchange Intermediate Confirmation Report |  | DSO
Imbalance prices per Market Balance Area (MBA) | Production and consumption imbalance prices per MBA | BRP
Production per production unit (PU) (evening) | All productions per production unit under BRP's balance responsibility | BRP
Production per production unit (PU) | All productions per production unit under BRP's balance responsibility | BRP
Production per production unit (PU) | All DSO's productions per production unit (PU) | DSO
Production plan per BRP and RO | All BRP's production plans per RO | BRP
PX Market Flow TSO | PX Market Flows reported by NEMOs | TSO
PX Market Flow TSO 2 | PX Market Flows reported by NEMOs | TSO
PX Trades - Day-ahead | PX Trades - Day-ahead | BRP
PX Trades - Day-ahead (NSL) | PX Trades - Day-ahead (NSL) | BRP
PX Trades - Intraday | PX Trades - Intraday | BRP
Secondary Frequency Restoration Reserves (FRR) | All BSP's activated reserves of type FRR-A (Frequency Restoration Reserve - Automatic). FRR-A is an automatic reserve, activated continuously by the frequency. | BSP
Tertiary Replacement Reserves (RR) | All BSP's activated reserves of type RR (Tertiary Control) e.g. FRR-M reserves | BSP
Primary Frequency Containment Reserves (FCR) | All BSP's activated reserves of type FCR (Frequency Containment Reserve). FCR is an automatic and momentarily regulation, to adjust the physical balance in the power system. | BSP
Imbalance prices per Market Balance Area (MBA) | Production and Consumption imbalance prices per MBA | BSP

## Slide 14: Specific data packages; 15 min values on a daily basis 4/5
Data Package | Description | MP Role
Load Profile per MGA | System selects all MGAs in Sweden. | BRP
Load Profile per MGA | System selects all MGAs in Sweden. | DSO
Load Profile per own MGA | Load profiles for MGAs related to DSO. Defined by MGA-DSO relation. | DSO
Load Profile per own MGA | Load profiles for MGAs where BRP has existing Loadshare MEC. BRP is Loadshare MEC attribute. | BRP
Load Profile per MBA per BRP | Aggregated Load Profiles per MBA per BRP. | BRP
Profiled Consumption per MGA per BRP | Profiled Consumption per MGA per BRP. BRP is a Consumption MEC attribute. General and Losses (if there are any) Consumption are displayed as separate value. Month aggregation. | BRP
Preliminary Loadshare per MGA per BRP per Type | Loadshares reported for BRP. General and Losses (if there are any) Loadshares are displayed as separate value. Month aggregation | BRP
Final Loadshare per MGA per BRP per type | System selects Total Final Loadshares per MGA where BRP has a Loadshare MEC. BRP is Loadshare MEC attribute. Month aggregation. | BRP
Profiled Imbalance per MGA | System selects BRP with Profiled Imbalance per MGA. BRP with Loadshare MEC Cons Bus Type = Losses. Month aggregation. | BRP
Reconciliation Quantity and Amount per MGA per BRP | Reconciliation Quantity and Amount per MGA per BRP, Month aggregation. | BRP
Reconciliation Quantity and Amount per Country per BRP | DP contains BRP Reconciliation results for respective Country, calculations are per couple BRP and Country: Bought Reconciliation Quantity, Sold Reconciliation Quantity, Bought Reconciliation Amount, Sold Reconciliation Amount, Month aggregation. | BRP
Invoiced Reconciliation Quantity and Amount per MGA per BRP | Reconciliation Quantity and Amount per Country per BRPonciliation results for all respective MGAs. Triggered within Invoicing process. Month aggregation. | BRP
Reconciliation Price | Reconciliation Price per MBA. | BRP
Profiled Consumption per MGA per BRP | Aggregated monthly Profiled Consumption per MGA per BRP. BRP is a Consumption MEC attribute. General and Losses (if there are any) Consumption are displayed as separate value. Month aggregation. | BRP

## Slide 15: Specific data packages; 15 min values on a daily basis 5/5
Data Package | Description | MP Role
Delivered Reserves for BSP | Energy up/down for BSP per MBA/MGA, market party, RO, Balancing Sub-Service and Activation Method | BSP
Delivered Reserves for BRP | Energy up/down for BSP per MBA/MGA, market party, RO, Balancing Sub-Service and Activation Method | BRP
Reserve Compensations for BSP per RE, MGA and Balancing Service | BSP's Reserve Compensations per RE volumes (MWh) and amounts (EUR) per MGA and Balancing Sub-Service | BSP
Reserve Compensations for BRP per RE, MGA and Balancing Service | BRP's Reserve Compensations per RE volumes (MWh) and amounts (EUR) per MGA and Balancing Sub-Service | BRP
Regulation Imbalance for BSP per MBA | BSP's Regulation Imbalance per MBA volumes (MWh) and amounts (EUR) | BSP

## Slide 16: Generic data packages for BRPs; hourly values on a daily basis 1/2
Data Package | Description
Consumption per BRP and MBA | Consumption per BRP and MBA
Consumption per type per BRP and MBA | Consumption per type per BRP and MBA
Consumption per RE and MGA | Consumption per RE and MGA
Production Minor per BRP and MBA | Production Minor per BRP and MBA
Production Plan per BRP and MBA | Production Plan per BRP and MBA
Bilateral Trade Purchase per BRP and MBA | Bilateral Trade Purchase per BRP and MBA
Bilateral Trade Sales per BRP and MBA | Bilateral Trade Sales per BRP and MBA
Day-ahead Purchase per BRP and MBA | Day-ahead Purchase per BRP and MBA
Day-ahead Sales per BRP and MBA | Day-ahead Sales per BRP and MBA
Intraday Purchase per BRP and MBA | Intraday Purchase per BRP and MBA
Intraday Sales per BRP and MBA | Intraday Sales per BRP and MBA
Day-ahead Flow Import per BRP and MBA | Day-ahead Flow Import per BRP and MBA

## Slide 17: Generic data packages for BRPs; hourly values on a daily basis 2/2
Data Package | Description
Day-ahead Flow Export per BRP and MBA | Day-ahead Flow Export per BRP and MBA
Intraday Flow Import per BRP and MBA | Intraday Flow Import per BRP and MBA
Intraday Flow Export per BRP and MBA | Intraday Flow Export per BRP and MBA
MGA Imbalance Surplus per BRP and MBA | MGA Imbalance Surplus per BRP and MBA
MGA imbalance Deficit per BRP and MBA | MGA imbalance Deficit per BRP and MBA
Consumption Imbalance Adjustment Up per BRP and MBA | Consumption Imbalance Adjustment Up per BRP and MBA
Consumption Imbalance Adjustment Down per BRP and MBA | Consumption Imbalance Adjustment Down per BRP and MBA
MGA Trade Import per BRP and MBA | MGA Trade Import per BRP and MBA
MGA trade Export per BRP and MBA | MGA trade Export per BRP and MBA
Consumption Pump Storage per BRP and MBA | Consumption Pump Storage per BRP and MBA
Normal Production per BRP and MBA | Normal Production per BRP and MBA
Production Imbalance Adjustment Up per BRP and MBA | Production Imbalance Adjustment Up per BRP and MBA
Production imbalance Adjustment Down per BRP and MBA | Production imbalance Adjustment Down per BRP and MBA
Day-ahead (NSL) Purchase per BRP and MBA | Day-ahead (NSL) Purchase per BRP and MBA
Day-ahead (NSL) Sales per BRP and MBA | Day-ahead (NSL) Sales per BRP and MBA
Day-ahead (NSL) Flow Import per BRP and MBA | Day-ahead (NSL) Flow Import per BRP and MBA
Day-ahead (NSL) Flow Export per BRP and MBA | Day-ahead (NSL) Flow Export per BRP and MBA

## Slide 18: Generic data packages for BRPs; 15 min values on a daily basis 1/3
Data Package | Description
Consumption per BRP and MBA 15-minute | Consumption per BRP and MBA
Consumption per type per BRP and MBA 15-minute | Consumption per type per BRP and MBA
Consumption per RE and MGA 15-minute | Consumption per RE and MGA
Production Minor per BRP and MBA 15-minute | Production Minor per BRP and MBA
Production Plan per BRP and MBA 15-minute | Production Plan per BRP and MBA
Bilateral Trade Purchase per BRP and MBA 15-minute | Bilateral Trade Purchase per BRP and MBA
Bilateral Trade Sales per BRP and MBA 15-minute | Bilateral Trade Sales per BRP and MBA
Day-ahead Purchase per BRP and MBA 15-minute | Day-ahead Purchase per BRP and MBA
Day-ahead Sales per BRP and MBA 15-minute | Day-ahead Sales per BRP and MBA
Intraday Purchase per BRP and MBA 15-minute | Intraday Purchase per BRP and MBA
Intraday Sales per BRP and MBA 15-minute | Intraday Sales per BRP and MBA
Day-ahead Flow Import per BRP and MBA 15-minute | Day-ahead Flow Import per BRP and MBA
Day-ahead Flow Export per BRP and MBA 15-minute | Day-ahead Flow Export per BRP and MBA

## Slide 19: Generic data packages for BRPs; 15 min values on a daily basis 2/2
Data Package | Description
Intraday Flow Import per BRP and MBA 15-minute | Intraday Flow Import per BRP and MBA
Intraday Flow Export per BRP and MBA 15-minute | Intraday Flow Export per BRP and MBA
MGA Imbalance Surplus per BRP and MBA 15-minute | MGA Imbalance Surplus per BRP and MBA
MGA imbalance Deficit per BRP and MBA 15-minute | MGA imbalance Deficit per BRP and MBA
Consumption Imbalance Adjustment Up per BRP and MBA 15-minute | Consumption Imbalance Adjustment Up per BRP and MBA
Consumption Imbalance Adjustment Down per BRP and MBA 15-minute | Consumption Imbalance Adjustment Down per BRP and MBA
MGA Trade Import per BRP and MBA 15-minute | MGA Trade Import per BRP and MBA
MGA trade Export per BRP and MBA 15-minute | MGA trade Export per BRP and MBA
Consumption Pump Storage per BRP and MBA 15-minute | Consumption Pump Storage per BRP and MBA
Normal Production per BRP and MBA 15-minute | Normal Production per BRP and MBA
Production Imbalance Adjustment Up per BRP and MBA 15-minute | Production Imbalance Adjustment Up per BRP and MBA
Production imbalance Adjustment Down per BRP and MBA 15-minute | Production imbalance Adjustment Down per BRP and MBA
Day-ahead (NSL) Purchase per BRP and MBA 15-minute | Day-ahead (NSL) Purchase per BRP and MBA
Day-ahead (NSL) Sales per BRP and MBA 15-minute | Day-ahead (NSL) Sales per BRP and MBA
Day-ahead (NSL) Flow Import per BRP and MBA 15-minute | Day-ahead (NSL) Flow Import per BRP and MBA
Day-ahead (NSL) Flow Export per BRP and MBA 15-minute | Day-ahead (NSL) Flow Export per BRP and MBA

## Slide 20: Generic data packages for BRPs; 15 min values on a daily basis 3/3
Data Package | Description
Day-ahead (NSL) Purchase per BRP and MBA 15-minute | Day-ahead (NSL) Purchase per BRP and MBA
Day-ahead (NSL) Sales per BRP and MBA 15-minute | Day-ahead (NSL) Sales per BRP and MBA
Day-ahead (NSL) Flow Import per BRP and MBA 15-minute | Day-ahead (NSL) Flow Import per BRP and MBA
Day-ahead (NSL) Flow Export per BRP and MBA 15-minute | Day-ahead (NSL) Flow Export per BRP and MBA
Day-ahead Flow Export per MBA and PX Market (NSL) 15-minute | Day-ahead Flow Export per MBA and PX Market (NSL)
Day-ahead Flow Import per MBA and PX Market (NSL) 15-minute | Day-ahead Flow Import per MBA and PX Market (NSL)